Shell and Tube Heat Exchanger Experiment

Introduction

The process of heat exchange between two fluids which are at different temperatures and flow rates occurs in many engineering applications. Several types of heat exchangers have been widely used in the industry. Shell-and-Tube heat exchangers are among the common types of heat exchangers.  A basic schematic for a single pass shell-and-tube heat exchanger is shown in Figure 1.  The stream to be cooled enters the tube side and is distributed amongst the tubes shown with red arrows.  The stream that cools the liquid is shown in blue enters on the shell-side and flows perpendicular to the tube bundle for maximum heat transfer.  The shell-side flow passes around baffles placed around the tube bundle in order to increase both the residence time of the fluid around the tube bundle as well as to promote turbulence in order to maximize the efficiency of the heat exchanger. Heat exchangers are typically classified according to flow arrangement. In the parallel-flow heat exchanger, the hot and cold fluids enter at the same end, flow in the same direction, and leave at the same end. In the counter-flow arrangement, the hot and cold fluids enter the heat exchanger at different ends and flow in opposite directions. Each fluid arrangement leads to different heat rates and the calculations are different accordingly [1].

Figure 1 Schematic of a Single-Pass Shell-and-Tube Heat Exchanger with Parallel-Flow Configuration

Figure 2 Experimental Apparatus

Figure 2 illustrates the Heat Exchanger experiment apparatus.  Based on long-term setup of the apparatus, the hot flow passes through the tube and the cold flow passes through the shell. Different configuration of valves can result in parallel and counter flows.  The hot and cold flow rates are measured by two flow meters, located along the incoming flows.

In order to measure the temperature of fluids and heat transfer surfaces, ten thermocouples have been installed in this apparatus. The measured temperature of each thermocouple is shown on the readout when the selector switch points to the thermocouple number. The thermocouples are located in different positions to measure the temperatures according to Table 1.

Table1. Thermocouples

| Thermocouple | Measured Temperature | Thermocouple | Measured Temprature |
| --- | --- | --- | --- |
| 1 | Tube Inlet | 5 | Shell Inlet |
| 2 | Tube-side heat transfer surface at 16” * | 6 | Shell-side heat transfer surface at 16” * |
| 3 | Tube-side heat transfer surface at 19” * | 7 | Shell-side heat transfer surface at 19” * |
| 4 | Tube-side heat transfer surface at 21” * | 8 | Shell-side heat transfer surface at 21” * |
| 10 | Tube Outlet | 9 | Shell Outlet |

* measured from the tube side.

Laboratory Procedure:

Parallel Flow Experimental Setup

- Open the valves 1, 3, 4, 6, and 7 all the way.

- Close valves 2 and 5.

- Turn on the main power.

- Turn on hot and cold water supply all the way.

- Close valve 1 until it reads 2 GPM.

- Close valve 3 until it reads 20% (2 GPM).

- Wait at least 15 minutes so that the system reaches steady state.

- Record temperatures of the system at steady state according to Table 2.

- Turn off the hot and cold water supplies.

- Proceed to the next configuration.

Counter Flow Experimental Setup

- Open valves 1, 2, 3, 5, and 7 all the way.

- Close valves 4 and 6.

- Turn on the hot and cold water supplies all the way.

- Close valve 1 until it reads 3 GPM.

- Close valve 3 until it reads 30% (3 GPM).

- Wait at least 15 minutes so that the system reaches steady state.

- Record temperatures of the system at steady state according to Table 3.

Shut Down

- Turn off the hot and cold water supplies.

- Unplug the electrical cord.

- Open all valves fully and wait until water stops draining from the apparatus.

- Close all valves fully.

Questions

- Calculate the mass flow rate of each flow for both experiments and write the values in Table 2 and 3.

- Calculate the heat lost by hot flow for both experiments using  , cp = 4.178 kJ/kg.K

- Calculate the heat gained by cold flow for both experiments and compare them with question in 2 above.

- Calculate the average surface temperature of tube side and shell-side for both experiments. Note that Ts,hot = (T2+T3+T4)/3 and Ts,cold = (T6+T7+T8)/3.

Considering a constant surface temperature, calculate the Logarithmic Mean Temperature Difference for tube and shell-sides in both experiments. Note that

,

- Calculate the convective heat transfer coefficient in shell and tube sides. Note that h = A ΔTLM  / q.

- Which side has larger convective heat transfer coefficient and why?

- Calculate the over heat transfer coefficient of the heat exchanger for both experiments. Note that the overall heat transfer coefficient of the heat exchanger is calculated from.

- Calculate the heat exchanger effectiveness for both experiments and compare them with each other. Effectiveness is

- The Number of Transfer Units (NTU) can be calculated in terms of exchanger effectiveness as follows:

Parallel flow:

Counter flow:

,

Calculate NTU for both experiments.

- According to definition, NTU = UA/ Cmin. . Using this equation, calculate the over heat transfer coefficient of the heat exchanger, U, and compare it with question 7.

References

[1] Incropera, DeWitt, Bergman, Lavine. (2007) “Introduction to Heat Transfer 5th Edition” John Wiley, New York

Table 2 Parallel flow arrangement

| Hot fluid mass flow rate (kg/s) |  | Cold fluid mass flow rate (kg/s) |  |
| --- | --- | --- | --- |
| Thermocouple | T1 | T2 | T3 | T4 | T5 | T6 | T7 | T8 | T9 | T10 |
| ºF |  |  |  |  |  |  |  |  |  |  |
| ºC |  |  |  |  |  |  |  |  |  |  |

Table 3 Counter flow arrangement

| Hot fluid mass flow rate (kg/s) |  | Cold fluid mass flow rate (kg/s) |  |
| --- | --- | --- | --- |
| Thermocouple | T1 | T2 | T3 | T4 | T5 | T6 | T7 | T8 | T9 | T10 |
| ºF |  |  |  |  |  |  |  |  |  |  |
| ºC |  |  |  |  |  |  |  |  |  |  |

Table 4 Heat Exchanger Geometry Data

| Heat Exchanger Surface Area | 0.79 m2 |
| --- | --- |
| Tube Diameter | 0.25 in. |
| Number of Tubes | 112 |
| Shell Diameter | 4.13 in. |
| Tube Length | 14 in. |
| Water Density | 995 kg/m3 |

# Text boxes

Tube-side

Outlet

Thermocouple Selector and Readout

Main Power

Shell and Tube Heat Exchanger

Parallel Flow Outlet

Shell-side Inlet

Counter Flow Outlet

Tube-side Inlet

Flow meters

Tube-Side Inlet

Tube-Side Outlet

Shell-Side Inlet

Shell-Side Outlet