## Slide 1: ECE 404
PCB Design Presentation
-Deependra Mishra

## Slide 2: Overview
Introduction – Why PCB?
Materials of PCB
Parts of PCB
Jumpers
Solder Mask
Silkscreen
Multilayer PCB
Physical Design Issues
Design Software
Material Required to Design PCB
Steps in PCB Design

## Slide 3: Introduction
Printed circuit board
Mechanical support
Electrically connect electronic components using conductive pathways, or traces
PCB populated with electronic components is a printed circuit assembly (PCA)

## Slide 4: Why PCB?
Rugged, inexpensive, and can be highly reliable
Faster (due to automation) and consistent in high volume production
Professional(more neater look)

## Slide 5: Example of wire wrapping circuit board

## Slide 6: Materials of PCB
Conducting layers are typically made of thin copper foil.
The board is typically coated with a solder mask that is green in color. Other colors that are normally available are blue and red.
Unwanted copper is removed from the substrate after etching leaving only the desired copper traces or pathways

## Slide 7: Different Layers

## Slide 8: Parts of a PCB
Components
Pads
Traces
Vias
Top Metal Layer
Bottom Metal Layer

## Slide 9: Components
Components are the actual devices used in the circuit.
This includes input/output connections.
I/O ports, including power supply connections, are also important in the PCB design.

## Slide 10: Components

## Slide 11: Pads
Location that components connect to.
You will solder components to the pads on the PCB.
Pads will connect to traces.
Pads have an inner diameter and outer diameter.

## Slide 12: Pads and Trace

## Slide 13: Traces
Traces connect pads together.
Traces are essentially the wiring of the PCB.
Equivalent to wire for conducting signals
Traces sometimes connect to vias.
High current traces should be wide.
Signal traces usually narrower than power or ground traces

## Slide 14: Vias
Pad with a plated hole connecting traces from one layer of board to other layers.
Attempt to minimize via use in your PCBs.
Some component leads can be used as vias.

## Slide 15: Vias
Blind Via
Buried Via
Through hole Via

## Slide 16: Top Metal Layer
Most of the components reside on the top layer
Fewer traces on the top layer
Components are soldered to the pads on the top layer of PCB
Higher circuit densities

## Slide 17: Bottom Metal Layer
Few components on this layer.
Many traces on this layer.
Most soldering done on this layer.

## Slide 18: Jumpers
Often, many signal wires need to exist in too small of a space and must overlap.
Running traces on different PCB layers is an option.
Multilayer PCBs are often expensive.
Solution: use jumpers

## Slide 19: Jumpers

## Slide 20: Solder Mask
Protect copper traces on outer layers from corrosion
Areas that shouldn't be soldered may be covered with polymer resist solder mask coating
Designed to keep solder only in certain areas
Prevents solder form binding between conductors and thereby creating short circuits(i.e. hides traces from solder)

## Slide 21: Soldering
Wave Soldering- for through hole and SMT
Reflow Soldering- for SMT

## Slide 22: Silkscreen
Printing on the solder mask to designate component locations
Readable information about component part numbers and placement.
Helpful in assembling, testing and servicing the circuit board.

## Slide 23: Multilayer PCBs
More then a top and bottom layer.
Typically there will be a power plane, ground plane, top layer, and bottom layer.
Sometimes signal layers are added as needed.
Sometimes RF planes made of more expensive materials are added.

## Slide 24: Physical Design Issues
Component Size
Heat Dissipation
Input and Output
Mounting Points

## Slide 25: Component Size
Make sure components will actually fit.
This especially applies for circuits that require high component densities.
Some components come in multiple sizes. SMT vs Through Hole
Sometimes you can get tall and narrow caps or short and wide capacitors.

## Slide 26: Heat Dissipation-Heat Sinks
Heat sink dissipates heat off the component
Does not remove heat, just moves it
Some components get hot, requiring heat sink
Data sheets specify the size of the heat sink
A short circuit may result when two devices share the same heat sink

## Slide 27: Mounting Points
PCB needs to be mechanically secured
  To chassis-consist of metal frame on which the circuit boards and other electronic components are mounted
  To another PCB/socket on PCB
  To attachments to a heatsink

## Slide 28: Parasitics
High frequency circuits
  Series Inductance
  Shunt Capacitance
  Inductive Coupling
  Capacitive Coupling

## Slide 29: Series Inductance
Not an issue for low frequency circuits(<10 Mhz)
Inductance of a trace may be significant
Power connections - add shunt capacitor to counter the series inductance of a long trace
Capacitor has a low AC impedance
A 100nF capacitor is often used along with a larger capacitor. 100 nF ceramics have very low impedance at higher frequencies.

## Slide 30: Shunt Capacitance
Result of wide wires over a ground plane.
Limits speed of circuits, including digital circuits
Insignificant for low performance circuits
Capacitor from voltage to ground will minimize

## Slide 31: Inductive Coupling
Transfer of energy from one circuit component to another through shared magnetic field
Change in current flow through one device induces current flow in other device
Current flow in one trace induces current in another trace
Minimize the long parallel runs of traces
Run traces perpendicular to each other

## Slide 32: Capacitive Coupling
Transfer of energy in electrical n/w due to capacitance between circuit nodes
Minimizing long traces on adjacent layers will reduce capacitive coupling
Ground planes are run between the signals that might affect each other.

## Slide 33: Routing

## Slide 34: Trace connection with Pads

## Slide 35: Pre-work
Thoroughly simulate your circuit-make sure the circuit worked in simulations
Thoroughly test the prototype-make sure the circuit worked on the bread board
Have all the data sheets handy for all components
Try various component configurations

## Slide 36: Simulations
Important to simulate the circuits before building them
Allow margin for component tolerances
Avoid using precise components. e.g a PWM controller that requires exact 10 V DC to work and will fail if there is 10.01V
High performance circuits or SMT devices require PCBs and should be simulated extensively first

## Slide 37: Transferring your design to a board
Direct Transfer using marker
"Press-N-Peel" sheets and Variations use of heat
Blender pen
Photolithography use of UV light

## Slide 38: Design Software
PCB Artist
CadSoft EAGLE
PCBWizard
OrCAD etc
Gerber files: describe the images of a printed circuit board (copper layers, solder mask, legend, etc.) as well as the drilling and milling data, de facto standard used by industry to describe PCB images

## Slide 39
Example Gerber files
Notes: Example Gerber layers, showing the top overlay (legend), top solder resist (protective film), top layer copper traces, and bottom layer copper traces of a printed circuit board.

## Slide 40: Materials Required to make PCB
Notes: Other Materials: Permanent black marker, blade cutter, sandpaper, kitchen paper, cotton wool, some old clothes.

## Slide 41: Steps in PCB design
Step 1: Take printout of PCB layout
Using laser printer & glossy paper
Mirror image
Step 2: Cutting the copper plate

## Slide 42: Steps in PCB design
Step 3: Make it smooth
Rub the copper side
Removes top oxide layer and photo resist layer
Sanded surface allow image to stick better

## Slide 43: Steps in PCB design
Step 4: Printing Design layout to board
Method 1: Iron on glossy paper ( transfers the toner)
Method 2: Circuit by hand (using marker)

## Slide 44: Steps in PCB design
Step 5: Apply heat (Iron it !!)
Iron it image down to copper side
Apply little pressure for 10-15 min
Iron heat transfer toner to cooper plate
CAUTION: Do not directly touch copper plate because it is very hot due to ironing.

## Slide 45: Steps in PCB design
Step 6: Peeling
Place printed plate in Luke warm water (10 min)
Remove the paper
Use black marker to dark lighted track

## Slide 46: Steps in PCB design
Step 7: Etching
Dissolve 2-3 tea spoon ferric chloride in water
Dip PCB in etching solution for 30 min
FeCl3 reacts with unmasked Cu and removes unwanted Cu
Cu + FeCl3 = CuCl3 + Fe

## Slide 47: Steps in PCB design
Step 8: Apply thinner ( Final touch)
Few drops of thinner (acetone or nail polish) on pinch of cotton will remove the remaining toner
Rinse carefully and dry with a clean cloth

## Slide 48: Steps in PCB Design
Step 9: Drill holes and apply Solder Mask
Apply solder mask area to entire board with the exception of solder pads

## Slide 49: Steps in PCB Design
Step 10. Solder Coat
Step 11: Silkscreen
Apply white letter marking using screen printing process
Apply solder to pads
http://www.youtube.com/watch?v=Q6WJqjVleG0&feature=related
http://www.advancedcircuits.com/

## Slide 50: WEBSITES
http://www.advancedcircuits.com
How to download the software (EAGLE Layout editor)
Go to http://www.cadsoftusa.com
Click ‘Freeware’
Click ‘Download’
Find the correct version (Windows/Linux,English)
Also download Manual and Tutorial

## Slide 51: References
PCB Design slides by Jakia Afruz
www.wikipedia.org
www.pcbexpress.com
A Practical Guide to high-speed printed circuit board layout