## Slide 1: ECE 404 PCB Design.

## Slide 2: By Julian Rene Cuellar Buritica
Guided by
Dr. Scott Umbaugh
Graduate Program Director
Department of Electrical & Computer Engineering
Southern Illinois University - Edwardsville

## Slide 3: Overview
Introduction – Why PCB?
Materials of PCB
Parts of PCB
  Jumpers
  Solder Mask
  Silkscreen
Multilayer PCB
Physical Design Issues
Design Software
Material Required to Design PCB
Manual PCB Design
PCB Manufacturing Companies

## Slide 4: Introduction
Printed Circuit Board
Mechanical support
Electrically connect electronic components using conductive pathways, or traces
PCB populated with electronic components is a printed circuit assembly (PCA)

## Slide 5: Why PCB?
Rugged, inexpensive, and can be highly reliable
Faster (due to automation) and consistent in high volume production
Professional(more neater look)
Notes: (fuertestrong, sharp, hard, loud, heavy, rugged)

## Slide 6: Wire wrapping circuit board
BreadBoard
PCB

## Slide 7: Materials of PCB
Conducting layers are typically made of thin copper foil.
The board is typically coated with a solder mask that is green in color. Other colors that are normally available are blue and red.
Unwanted copper is removed from the substrate after etching leaving only the desired copper traces or pathways
Notes: copper clad laminate board

## Slide 8: Dielectric PCB Layer
Most common material for PCB is the FR-4 board:
  FR stands for Flame Retardant.
  Composite material with woven fiberglass cloth with an epoxy resin binder.
  Thickness of FR-4 and copper specified separately.
  Copper foil thickness in (oz/ft^2), [simply ounce].
    1 oz/ft^2 copper foil has a thickness of 35 µm.
    1/0 - 1 oz/ft^2 copper one side, with no on the other.
    1/1 - denotes 1 oz/ft^2 copper on both sides.
Notes: Grade designations for glass epoxy laminates are: G10, G11, FR4, FR5 and FR6. Of these, FR4 is the grade most widely in use today. G-10, the predecessor to FR-4, lacks FR-4's self-extinguishing flammability characteristics. Hence.

## Slide 9: Different Layers of PCB

## Slide 10
Notes: prepreg (from pre-impregnated) is fibreglass impregnated with resin. Prepregsare thus fibreglass strengthened by an adhesive layer (similar to FR4 material)

## Slide 11: Parts of a PCB
Components
Pads
Traces
Vias
Top Metal Layer
Bottom Metal Layer

## Slide 12: Components
Components are the actual devices used in the circuit.
This includes input/output connections.
I/O ports, including power supply connections, are also important in the PCB design.

## Slide 13: Components

## Slide 14: Pads
Location that components connect to.
You will solder components to the pads on the PCB.
Pads will connect to traces.
Pads have an inner diameter and outer diameter.

## Slide 15: Pads and Trace

## Slide 16: Traces
Traces connect pads together.
Traces are essentially the wiring of the PCB.
Equivalent to wire for conducting signals
Traces sometimes connect to vias.
High current traces should be wide.
Signal traces usually narrower than power or ground traces

## Slide 17: Vias
Pad with a plated hole connecting traces from one layer of board to other layers.
Attempt to minimize via use in your PCBs.
Some component leads can be used as vias.

## Slide 18: Vias
Blind Via
Buried Via
Through hole Via

## Slide 19: Top Metal Layer
Most of the components reside on the top layer
Fewer traces on the top layer
Components are soldered to the pads on the top layer of PCB
Higher circuit densities

## Slide 20: Bottom Metal Layer
Few components on this layer.
Many traces on this layer.
Most soldering done on this layer.

## Slide 21: Jumpers
Often, many signal wires need to exist in too small of a space and must overlap.
Running traces on different PCB layers is an option.
Multilayer PCBs are often expensive.
Solution: Use jumpers

## Slide 22: Jumpers

## Slide 23: Solder Mask
Protect copper traces on outer layers from corrosion
Areas that shouldn't be soldered may be covered with polymer resist solder mask coating
Designed to keep solder only in certain areas
Prevents solder form binding between conductors and thereby creating short circuits(i.e. hides traces from solder)

## Slide 24: Soldering
Wave Soldering- for through hole and SMT
Reflow Soldering- for SMT

## Slide 25: Silkscreen
Printing on the solder mask to designate component locations
Readable information about component part numbers and placement.
Helpful in assembling, testing and servicing the circuit board.

## Slide 26: Multilayer PCBs
More than a top and bottom layer.
Typically there will be a power plane, ground plane, top layer, and bottom layer.
Sometimes signal layers are added as needed.
Sometimes RF planes made of more expensive materials are added.

## Slide 27: Physical Design Issues
Component Size
Heat Dissipation
Input and Output
Mounting Points

## Slide 28: Component Size
Make sure components will actually fit.
This especially applies for circuits that require high component densities.
Some components come in multiple sizes. SMT vs Through Hole
Sometimes you can get tall and narrow caps or short and wide capacitors.

## Slide 29: Heat Dissipation-Heat Sinks
Heat sink dissipates heat off the component
Does not remove heat, just moves it
Some components get hot, requiring heat sink
Data sheets specify the size of the heat sink
A short circuit may result when two devices share the same heat sink

## Slide 30: Mounting Points
PCB needs to be mechanically secured
  To chassis-consist of metal frame on which the circuit boards and other electronic components are mounted
  To another PCB/socket on PCB
  To attachments to a heatsink

## Slide 31: Parasitics
High frequency circuits
  Series Inductance
  Shunt Capacitance
  Inductive Coupling
  Capacitive Coupling

## Slide 32: Series Inductance
Not an issue for low frequency circuits(<10 Mhz)
Inductance of a trace may be significant
Power connections - add shunt capacitor to counter the series inductance of a long trace
Capacitor has a low AC impedance
A 100nF capacitor is often used along with a larger capacitor. 100 nF ceramics have very low impedance at higher frequencies.

## Slide 33: Series Inductance

## Slide 34: Shunt Capacitance
Result of wide wires over a ground plane.
Limits speed of circuits, including digital circuits
Insignificant for low performance circuits
Capacitor from voltage to ground will minimize

## Slide 35: Shunt Capacitance
Capacitance | Reference [1] | EMS
Between the left trace and the ground plane | -4.3047 pF | -4.3563 pF
Between the right trace and the ground plane | -4.3046 pF | -4.3552 pF
Between the two copper traces | -0.1673 pF | -0.1825 pF
https://www.emworks.com/application/inductance-capacitance-and-resistance-of-a-pcb-structure

## Slide 36: Power Planes

## Slide 37: Inductive Coupling
Transfer of energy from one circuit component to another through shared magnetic field
Change in current flow through one device induces current flow in other device
Current flow in one trace induces current in another trace
  Minimize the long parallel runs of traces
  Run traces perpendicular to each other

## Slide 38: Capacitive Coupling
Transfer of energy in electrical network due to capacitance between circuit nodes
Minimizing long traces on adjacent layers will reduce capacitive coupling
Ground planes are run between the signals that might affect each other.

## Slide 39: Capacitive/Inductive Reactances

## Slide 40: Routing

## Slide 41: Routing

## Slide 42: Trace connection with Pads

## Slide 43: Pre-work
Thoroughly simulate your circuit-make sure the circuit worked in simulations
Thoroughly test the prototype-make sure the circuit worked on the bread board
Have all the data sheets handy for all components
Try various component configurations

## Slide 44: Simulations
Important to simulate the circuits before building them
Allow margin for component tolerances
Avoid using precise components. e.g a PWM controller that requires exact 10 V DC to work and will fail if there is 10.01V
High performance circuits or SMT devices require PCBs and should be simulated extensively first

## Slide 45: Transferring your design to a board
Direct Transfer using marker
"Press-N-Peel" sheets and Variations use of heat
Blender pen
Photolithography use of UV light

## Slide 46: Design Software
Proteus Profesional
CADSoft EAGLE
PCBWizard
OrCAD …
Gerber files:
Describe the images of a printed circuit board (copper layers, solder mask, legend, etc.) as well as the drilling and milling data, de facto standard used by industry to describe PCB images
Notes: Full list on final slides…

## Slide 47: PCB Design

## Slide 48
Example Gerber files
Notes: Example Gerber layers, showing the top overlay (legend), top solder resist (protective film), top layer copper traces, and bottom layer copper traces of a printed circuit board.

## Slide 49: Materials Required to make PCB
Drill machine.
Cloth Iron.
Laser Printer.
Photo paper / Glossy paper.
Gloves.
Ferric Chloride (Etching solution)
PCB board.
Black permanent Marker.
Notes: Other Materials: Permanent black marker, blade cutter, sandpaper, kitchen paper, cotton wool, some old clothes.

## Slide 50: Manual PCB design
Step 1: Take printout of PCB layout
Using laser printer & glossy paper
Mirror image
Step 2: Cutting the copper plate

## Slide 51: Steps in PCB design
Step 3: Make it smooth
Rub the copper side
Removes top oxide layer and photo resist layer
Sanded surface allow image to stick better

## Slide 52: Steps in PCB design
Step 4: Printing Design layout to board
Method 1: Iron on glossy paper ( transfers the toner)
Method 2: Circuit by hand (using marker)

## Slide 53: Steps in PCB design
Step 5: Apply heat (Iron it !!)
Iron it image down to copper side
Apply little pressure for 10-15 min
Iron heat transfer toner to cooper plate
CAUTION: Do not directly touch copper plate because it is very hot due to ironing.

## Slide 54: Steps in PCB design
Step 6: Peeling
Place printed plate in Luke warm water (10 min)
Remove the paper
Use black marker to dark lighted track

## Slide 55: Steps in PCB design
Step 7: Etching
Dissolve 2-3 tea spoon ferric chloride in water
Dip PCB in etching solution for 30 min
FeCl3 reacts with unmasked Cu and removes unwanted Cu
Cu + FeCl3 = CuCl3 + Fe
Notes: Iron trichloride
Iron(III) chloride

## Slide 56: Steps in PCB design
Step 8: Apply thinner ( Final touch)
Few drops of thinner (acetone or nail polish) on pinch of cotton will remove the remaining toner
Rinse carefully and dry with a clean cloth

## Slide 57: Steps in PCB Design
Step 9: Drill holes and apply Solder Mask
Apply solder mask area to entire board with the exception of solder pads

## Slide 58: Steps in PCB Design
Step 10. Solder Coat
Step 11: Silkscreen
Apply white letter marking using screen printing process
Apply solder to pads
http://www.youtube.com/watch?v=Q6WJqjVleG0&feature=related

## Slide 59: PCB Design/Assembly Standards
  IPC-2221 (Generic Standard on Printed Board Design)
  J‐STD‐001 (Requirements for Soldered Electrical and Electronic Assemblies)
  IPC‐A‐630 (Standard for Manufacture, Inspection and Testing)
  IPC-A-610 (Acceptability/Inspection)
  IPC-J-STD-001 (How to build PCB/Meet 610)

## Slide 60: PCB Manufacturing Companies
  OSHPARK - https://oshpark.com/ (2 layer - $5/in^2)
  Advance Circuits 4PCB - https://www.4pcb.com/
  PCB Express - https://www.expresspcb.com/ (2 layer 2B- $9.85)
  Sunstone Circuits - https://www.sunstone.com/
  PCBCart - https://www.pcbcart.com/
  epec Engineered Technologies - https://www.epectec.com/
Notes: OSHPARK - (2 layer - $5/in^2)
PCB Express - (2 layer 2 Boards - $9.85)
Sunstone Circuits (2 layer 5 Boards - $64.05) – $12.81
https://www.pcbway.com/ from Ch:
4x4 in 2 layer 5 Units = 5 + 17 shipping = 22 (1-2 days shipping) <4.4 US>
4x4 in 2 layer 100 Units = 131 + 56 shipping = 187 (3-5 days shipping) <1.87 US>

## Slide 61: WEBSITES
http://www.advancedcircuits.com
https://www.orcad.com/
https://www.altium.com/
https://www.labcenter.com/
http://www.ipc.org/
https://www.flexiblecircuit.com/products/multi-layer-flex/
https://www.amitroncorp.com/?page_id=49

## Slide 62: EAGLE Layout editor
How to download the software (EAGLE Layout editor)
Go to http://www.cadsoftusa.com
Click ‘Freeware’
Click ‘Download’
Find the correct version (Windows/Linux, English)
Also download Manual and Tutorial

## Slide 63: References
PCB Design slides by Jakia Afruz
www.wikipedia.org
www.pcbexpress.com
A Practical Guide to high-speed printed circuit board layout