## Slide 1: Automatic Detection of Blood Vessels in Digital Retinal Image using CVIP Tools
Krishna Praveena Mandava
Sri Swetha Kantamaneni
Robert LeAnder

## Slide 2: Overview
The Devastation
  Diabetic retinopathy – 4.1 million US Adults
    National Health Interview Survey and US Census Population
  Glaucoma – 2 million individuals in the US.
Ophthalmologic images
  Important structures – Blood Vessels
  Help detect and treat Eye Diseases affecting blood vessels

## Slide 3: Overview
Damaged blood vessels indicate retinal disease.
  Blood clots indicate diabetic retinopathy.
  Narrow blood vessels indicate Central Retinal Artery Occlusion.
Observation of blood vessels in retinal images
  Shows presence of disease
  Helps prevent vision loss by early detection

## Slide 4: The Need for the Study
Automated Blood Vessel Extraction algorithms can save time, patients’ vision and medical costs.

## Slide 5: Effects of Diseases on Blood Vessels
Image of Diseased Retina Due to Diabetes
Disease produces hemorrhages, exudates and micro aneurysms (dark red spots).

## Slide 6: Central Retinal Artery Occlusion (CRAO)
Results in narrowing blood vessels.
Effects of Diseases on Blood Vessels

## Slide 7: Branch Retinal Artery Occlusion (BRAO)
Where artery branch points are occluded or blocked
Effects of Diseases on Blood Vessels

## Slide 8: 6 Approaches to Blood Vessel Extraction
Pattern recognition techniques
Model based approaches
Tracking based approaches
Artificial intelligence based approaches
Neural network based approaches
Miscellaneous tube-like object detection approaches.

## Slide 9
Pattern recognition techniques
Deals with automatic detection or classification of objects or features.
Multi scale approaches
Based on image resolution. Major vessels are extracted from low resolution images and minor vessels from high resolution images.
Skeleton based approaches
Vessel centerlines are extracted and then connected to create a vessel tree.
Ridge-Based Approaches
This is specialized skeleton based approaches. Ridges are peaks.
6 Approaches to Blood Vessel Extraction

## Slide 10
Region growing approaches…
  Assume that pixels are close to each other and have
  similar intensity values and are likely to belong to same
  objects.
        Start region growth from a seed point, then segment the image based on some predefined criterion.
  Have the Disadvantage that the seed point should be selected manually.
Differential-Geometry-based approaches…
  Utilizes techniques developed from the complex
  mathematical field of Differential Geometry
  Are based on blood-vessel structural properties
1. Pattern recognition techniques

## Slide 11
Matched-Filter Approaches
Are signal processing approaches where new images with un-extracted vessels are convolved with known profiles of vessels.
Matched filters are followed by image processing operations like
thresholding to get the final vessel contours.
Morphology Schemes…
Apply structuring elements to images to effect dilation and erosion are two main operations.
Include Top Hat and Watershed algorithms.
6 Approaches to Blood Vessel Extraction

## Slide 12
Model-Based Approaches…
Include Snakes algorithms, which are the primary types of algorithms used for vessel extraction.
A “Snake” is an active (deformable) contour with a set of Control Points
connecting the segments of the contour to each other.
It is a user interactive algorithm.
Tracking-Based Approaches…
Are similar to pattern recognition approaches except they apply local, instead of global operator
analyzing the pixels orthogonal to the tracking direction.
Artificial intelligence-based approaches…
Use prior knowledge of model vessel structures to determine vessel structures in the “unextracted” (unsegmented) image.
Some applications may use a general blood vessel model for extraction .

## Slide 13
Neural Network-Based approaches…
Use neural networks as a classification method. The system is trained using a set of images having blood vessel contours. The target image is
segmented using the trained system
Miscellaneous Tube-Like Object Detection Approaches…
Deals with the extraction of tubular structures from images.
Are not designed for vessel extraction.

## Slide 14
RETINAL BLOOD VESSEL EXTRACTION (SEGMENTATION)
Available Image Databases
DRIVE and STARE databases are available for the public.
http://www.ces.clemson.edu/~ahoover/stare/
http://www.parl.clemson.edu/stare/nerve/
We worked on 50 fundus images from the STARE database.
How the Images Were Taken
  An Optical camera is used to see through the pupil of the eye to the inner surface
of the eyeball. The resulting retinal image shows the optic nerve, fovea, and the blood vessels.

## Slide 15
Available Image Databases
DRIVE and STARE databases are available for the public.
http://www.ces.clemson.edu/~ahoover/stare/
http://www.parl.clemson.edu/stare/nerve/
We worked on 50 fundus images from the STARE database.
How the Images Were Taken
  An Optical camera is used to see through the pupil of the eye to the inner surface
of the eyeball. The resulting retinal image shows the optic nerve, fovea, and the blood vessels.

## Slide 16: Methods
Steps used blood vessel extraction…
Preprocessing
Extraction (segmentation)
Post processing
Software:
We used Computer Vision and Image Processing Tools to apply various algorithms to extract (segment) blood vessels.
Our Project

## Slide 17: Preprocessing:
Preprocessing will eliminate errors caused during taking the image and to reduce brightness effects on the image .
The original images are resized from 150*130 to 256*256 to use in CVIP tools.
Images in green bands show vessel structures most reliably. So, the green band was extracted.

## Slide 18: Extraction of blood vessels:
Tools that we applied:
Median filters
Laplacian filters
Image enhancement methods like Adaptive Contrast Enhancement, Histogram equalization.
Edge detection like Canny edge detection.

## Slide 19: Post processing:
The output images from blood vessel extraction were processed to get clearer contours of the vessels.
The following techniques were applied
  Sharpening by high pass spatial filters
  Smoothing by FFT smoothing, Ypmean filter

## Slide 20: Original Image and Expected Output:

## Slide 21
Our final images for different algorithms:
Exp 1
Exp 2
Exp 3
Exp 4
Exp 5

## Slide 22: Summary:
NEED AND USE: Extraction of blood vessels
Research is ongoing and there is still a great need to develop for an easier, more accurate and useful algorithms.
We were able to detect major blood vessels
Better algorithms can be developed using CVIP tools for the extraction of minor blood vessels.

## Slide 23: Suggestions for Future Work
Develop techniques for not only better detection of vessel edges, but for filling in the vessels so that they are more anatomically exacting regarding medical image standards. As only edges are detected they can be filled to get the blood vessel. Research should be done in filling the structures in our final outputs.
Develop better algorithms based advantages that may be given by the following vessel structural properties (as mentioned in a few papers):
Vessel size may decrease when moving away from the optic disc and the width of blood vessels may lie with in 2-10 pixels
Vessels are darker relative to the background.
The intensity profile varies from vessel to vessel by a small value. That profile is modeled as a Gaussian shape.

## Slide 24: More Suggestions for Future Work
Extraction of Minute blood vessels.
Extracted outputs can be verified by an ophthalmologist
Extraction outputs may also be calculated of sensitivity and specificity of blood vessels will give you better final results.
Detection of the optic disc is also needed as the border of the disc appears as a blood vessel. To prevent this the optic disc should be detected and removed before blood vessels are extracted.
Blood vessels should be separated from hemorrhages, and micro aneurysms.

## Slide 25: Conclusion:
CVIPtools is a very handy method for applying extraction techniques. There is a dire need for easier methods of blood vessel extraction. CVIPtools may provide accurate automatic detection algorithms for clinical applications in retinopathy.

## Slide 26: Reference:
1. Computer Imaging Digital Image Analysis and Processing
- Dr. Scott E Umbaugh
2. Digital Image Processing - Rafael C .Gonzalez, Richard
E .Woods
3. A Review of Vessel Extraction Techniques and Algorithms
– Cemil Kirbas and Francis Quek, Wright State University, Dayton, Ohio
4. Automated Diagnosis and Image understanding with Object Extraction, Object Classification and Inferencing in Retinal Images
–Micheal Goldbaum, Saied Moezzi, Adam Taylor, Shankar Chatterjee, Edward Hunter and Ramesh Jain ,University of California ,USA.

## Slide 27: Reference:
5. Characterization of the optic disc in retinal imagery using a probalistic approach
– Kenneth W.Tobin, Edward Chaum, Priya Govindaswami, Thomas P.Karnowski, Omer Sezer, University of Tennessee, Knoxville, Tennessee.
6. Blood Vessel Segmentation in Retinal Images
– P.Echevarria, T.Miller, J.O Meara
7. An improved matched filter for blood vessel detection of digital retinal images
– Mohammed Al-Rawi, Munib Qutaishat, Mohammed Arrar, University of Jordon,
Jordan.
8. Towards vessel characterization in the vicinity of the optic disc in digital retinal images – H.F.Jelinek,C.Lucas, D.J.Cornforth, W.Huang and M.J.Cree.
9. Retinal vessel segmentation using the 2-D Morlet Wavelet and Supervised classification
– Joao V.B.Soares, Jorge J.G. Leandro ,Robert M. Cesar-Jr., Herbert F. Jelinek and Micheal J.Cree, Senior Member IEEE
10. Locating blood vessels in retinal images by piece-wise threshold probing of a matched filter response
– Adam Hoover, Valentina Kouznetsova, Micheal Goldbaum

## Slide 28: Reference:
11. Automated identification of diabetic retinal exudates in digital color images
– A Osareh, M Mirmehdi, B Thomas, R Markham.
12.Survey of Retinal Image Segmentation and Registration
– Mai S. Mabrouk, Nahed H. Solouma and Yasser M.Kadah.
13.Automated detection of diabetic retinopathy on digital fundus images
– C. Sinthanayothin, J.F. Boyce, T.H. Williamson, H.L. Cook, E. Mensah, S. Lal and D. Usher.
14.Segmentation of retinal blood vessels by combining the detection of centerlines and morphological reconstruction
–Ana Maria Mendonca, Aurelio Campilho members IEEE.
15. The Eye Diseases Prevalence Research Group. The prevalence of diabetic retinopathy among adults in the united states. Archives of Ophthalmology, 122(4):552–563, 2004.
16. The Eye Diseases Prevalence Research Group. Prevalence of open-angle glaucoma among adults in the united states. Archives of Ophthalmology, 122(4):532–538, 2004.
17. Retinal Vessel Extraction Using Multiscale Matched Filters, Confidence and Edge Measures
Michal Sofka, and Charles V. Stewart

## Slide 29
THANK YOU