## Slide 1
ABSTRACT
QUANTITATIVE RESULTS
INTRODUCTION
Diabetes causes Diabetic Retinopathy (DR) by damaging the smaller retinal blood vessels which may lead to blindness. DR has three stages: Background Diabetic Retinopathy (BDR), Proliferate Diabetic Retinopathy (PDR) and Severe Diabetic Retinopathy (SDR) [3]. BDR is characterized by arteries that swell, weaken, become damaged and leak blood and serum deposits into the center of the retina. These deposits make the macula swell and decrease vision. The purpose of this study is to compare the effectiveness of two blood-vessel-segmentation algorithms and choose the best algorithm for refinement and application in the automatic detection of retinal blood vessels damaged in the BDR stage – the earliest stage of DR.
Comparison of two algorithms in the automatic segmentation of blood vessels in fundus images
ALGORITHM
Robert LeAnder, Myneni Sushma Chowdary, Swapnasri Mokkapati, and Scott E Umbaugh
SOUTHERN ILLINOIS UNIVERSITY EDWARDSVILLE
A. MATERIALS
Image Database: Fifteen color fundus images were collected from the Structured Analysis of the Retina (STARE) image database.
Hand-Drawn Images: Fifteen ophthalmologists’ hand-drawn tracings of the retinal blood vessels in the color fundus images mentioned above were downloaded from the STARE database. These were to be used as the “gold standard” of vessel segmentation and compared to the algorithm-output images to make an assessment of the segmentation effectiveness of those algorithms.
Software: The CVIPtools (Computer Vision and Image Processing) software package was used to perform the image processing operations as well as to calculate the differences between the hand-drawn images and the segmented images output by the two algorithms. Calculation tools in CVIPtools included Pratt’s Figure of Merit, Signal-to-Noise Ratio and Root Mean Square Error.
B. METHODS
Resizing Original Image: The images were resized from 150x130 to 300x260 pixels to provide greater visual clarity .
Green Band Extraction: The green band contains the greatest amount of contrast and is less affected by variations in illumination and consequently has the most pertinent visual information.
Preprocessing : Algorithms 1 and 2 differ in Preprocessing stage
Algorithm 1: Histogram stretch increases contrast between the blood vessels and the background and consequently improves the details and resolution of vessels.
A histogram stretch is followed by an opening operation whose morphological filter has a small structuring element of size 5. The opening operation helps obtain smooth blood vessels, while enhancing the vessels’ fundamental geometric properties. “Opening” opens up or expands holes, erodes edges and removes noise patterns. It also fills small holes in the vessels, while re-connecting disjoint vessel parts.
Algorithm 2 : The Yp mean filtering was chosen over other filters because it provided better noise removal and image smoothing.
Edge Detection (Algorithms 1 & 2): Both Algorithms 1 and 2 employed a Laplacian edge detector to extract the blood vessels’ features from the image.
Postprocessing : Algorithms 1 and 2 also differ in the postprocessing stage.
Algorithm 1: An opening operation using a morphological filter having a size-15 (large) rectangular structuring element extracted finer vessels, in addition to smoothing them. This second morphological-filtering step was done to separate objects that are connected by narrow strips, thereby eliminating extraneous peninsulas.
Algorithm 2 : Arithmetic Mean filter was used to eliminate noise. The Arithmetic Mean filter is a low pass filter that finds the average of the pixel values in its window, thereby smoothing out local variations within the image.
Not Operation : After the postprocessing stages (morphological and arithmetic mean filtering) in the algorithms, the images were converted from color to gray-scale and then binary thresholded using a threshold of 75. After that, a logical-Not operation was performed on the images.
Hough Transform (Algorithm 1) : Algorithm 1 extracted most of the major and minor vessels with some missing intersections and bifurcations. A Hough transform was then used to reintegrate the vessel segments. The Hough algorithm takes a collection of edge points (found by the edge detector) and finds all the lines on which the edge points lie.
Edge-Linking : Edge-linking was then performed to reconstruct missing vessel intersections. Edge-linking connects edge points to create line segments and boundaries.
Effective timing and treatment are critical to saving the sight of patients with diabetes. Lack of screening, as well as a shortage of ophthalmologists, contribute to approximately 8,000 cases per year of people who lose their sight to diabetic retinopathy, the leading cause of new cases of blindness [1] [2]. Timely treatment for diabetic retinopathy prevents severe vision loss in over 50% of eyes tested [1]. Fundus images can provide information for detecting and monitoring eye-related diseases, like diabetic retinopathy(indicated by damaged blood vessels), which if detected early, may help prevent vision loss [9]. So, early detection of damaged vessels in retinal images can provide valuable information about the presence of disease, thereby helping to prevent vision loss. Purpose: The purpose of this study was to compare the effectiveness of two blood vessel segmentation algorithms.
Methods: Fifteen fundus images from the STARE database were used to develop two algorithms. Fifteen more images derived from the first fifteen contained ophthalmologists’ hand-drawn tracings over the retinal vessels. The ophthalmologists’ tracings were used as the “gold standard” for perfect segmentation and compared with the segmented images that were output by the two algorithms. Comparisons between the segmented and the hand-drawn images were made using Pratt’s Figure of Merit (FOM), Signal-to-Noise Ratio (SNR) and Root Mean Square (RMS) Error. Results: Algorithm 2 has a 10% higher FOM and a 6% higher SNR than Algorithm 1, while having only 1.3% more RMS error than Algorithm 1. Conclusions: Algorithm 1 extracted most of the blood vessels with some missing intersections and bifurcations. Algorithm 2 extracted all the major blood vessels, but eradicated some vessels as well. Algorithm 2 outperformed Algorithm 1 in terms of visual clarity, FOM and SNR. The performances of these algorithms show that they have an appreciable amount of potential in helping ophthalmologists detect the severity of eye-related diseases and prevent vision loss.
MATERIALS AND METHODS
Morphological Opening-Operation
with size-5 rectangular structuring element
Morphological Opening-Operation
with size-15 rectangular structuring element
Original Image
Resize
Green Band Extraction
Histogram Stretch
Yp Mean filtering to remove
noise
Laplacian Edge Detection
Arithmetic Mean Filtering to remove noise
Color-to-Gray Conversion
Binary Thresholding
Not Operation
Hough Transform
Edge Linking
Final Image
Algorithm 1
Algorithm 2
Algorithm 1
Algorithm 2
Algorithm 1
Algorithm 2
PROCESSING RESULTS
Image A
Image B
Image C
Bar graph comparing Pratt’s Figures of Merit for retinal blood vessel segmentation using Algorithms 1 and 2 on 15 fundus images. The 15 sets of bars represent the performances of Algorithms 1 and 2 on 15 test images (see “Image Number” on the horizontal axis). The table’s two, bottom-most rows are the rounded FOM values for the two algorithms. FOM values > 0.5 has been approximated to 1 and FOM values < 0.5 have been approximated to 0.
Fig 39. Bar graph comparing the Root Mean Square (RMS) Errors for retinal blood vessel segmentation using Algorithms 1 and 2 on 15 fundus images. The 15 sets of bars represent the performances of Algorithms 1 and 2 on 15 test images (see “Image Number” on the horizontal axis). The table’s two, bottom-most rows are the rounded RMS values for the two algorithms.
Bar graph comparing the signal-to-noise ratios for retinal blood vessel segmentation using Algorithms 1 and 2 on 15 fundus images. The 15 sets of bars represent the performances of Algorithms 1 and 2 on 15 test images (see “Image Number” on the horizontal axis). The table’s two, bottom-most rows are the rounded SNR values for the two algorithms.
DISCUSSION
SUMMARY
CONCLUSION
The algorithms were applied to 15 fundus images from the STARE database and the results were compared with the hand-drawn images in the database. Algorithm 1 segmented the image by filling in objects’ holes and smoothing out their outlines. However, some of the intersections were deleted. We tried to reintegrate these missing intersections using the Hough transform. Although the Hough transform was applied, not all the missing vessels were reintegrated. Algorithm 2 extracted the blood vessels by histogram modification and edge detection, followed by mean filtering to remove the noise. The results were analyzed in terms of SNR (signal to noise ratio), RMS (root mean square) error and Pratt’s figure of merit. Because some of the vessels were missing, errors occur when the final images are compared with the binary-converted, hand-drawn images. These errors affected the signal strength. The outer ring artifact was not eliminated, consequently contributing to the noise. That is one primary reason for high values of RMS error in both the algorithms. The final outputs of the algorithms are binary images, whereas the hand-drawn images are color images. Consequently, the hand-drawn images were converted to binary format (color → grayscale → binary) at a gray-level threshold value of 75. During the course of the experiments, it was observed that better results could be achieved in terms of SNR, RMS error and FOM, if the outer ring was eliminated.
This paper proposed two algorithms for the automatic segmentation and detection of blood vessels in fundus images. The algorithms were developed using the CVIPtools imaging software package. Both algorithms have been applied to fifteen images. The major difference between the algorithms’ performances was that for both major and minor blood vessels, Algorithm 1 had difficulty segmenting intersections and bifurcations. Those junctions became lost in the output images. To recover them, we applied two reconstructive postprocesses, using the Hough transform (Algorithm 1) and edge linking (Algorithm 2). Although most of the major vessels’ junctions could be recovered using both algorithms, most of the minor vessels’ junctions could not. Algorithm 2 produced more consistent results in terms of clear, non-disjointed, segmented vessels. However, Algorithm 2 does have more “salt” noise in its output images.
Algorithm 1 extracted most of the major vessels, while Algorithm 2 extracted all of the major blood vessels and many of the minor ones.
From Figures 2-4, 6-8 and 10-12, it should be apparent by observation that both Algorithms 1 and 2 are extracting most (approximately 90-95%) of the vessels. Algorithm 2 has a 10%-higher FOM and a 6%-higher SNR, while having only 1.3% more RMS error than Algorithm 1. This comparatively-small amount of error is negligible.
REFERENCES
1. Teng, T., Lefley, M., Claremont, D., Progress towards automatic diabetic ocular screening: a review of image analysis and intelligent systems for diabetic retinopathy, Medical and Biological Engineering and Computing, Vol. 40(1): 2-13, 2002.
2. Meadows, M., Saving your sight: Early detection is critical, FDA Consumer Magazine, March-April 2002. http://www.fda.gov/fdac/features/2002/202_eyes.html.
3. Iqbal, M., Aibinu, A., Gubbal, N., Automatic Diagnosis of Diabetic Retinopathy Using Fundus Images (masters thesis), Bleking Institute of Technology, Karlskrona Sweden, 2006.
4. Umbaugh, S.E., Computer Imaging: Digital Image Analysis and Processing, Boca Raton: CRC Press, 2005.
5. Fang, B., Hsu, W., Lee, M.L., Reconstruction of vascular structure in retinal images, IEEE International Conference on Image Processing, Vol. 2, Sept 2003.
6. Zana, F., Klein, J.C., Segmentation of vessel-like patterns using mathematical morphology and curvature evaluation, Proceedings of Computer Assisted Radiology and Surgery, Vol. 1281, May 2005.
7. Al-Rawi, M., Qutaishat, M., Arrar, M., An improved matched filter for blood vessel detection of digital retinal images, Computers in Biology and Medicine, Vol. 37, Issue 2, February 2007.
8. Rapantzikos, K., Zervakis, M., Balas, K, Detection and segmentation of drusen deposits on human retina: Potential in the diagnosis of age-related macular degeneration, Medical Image Analysis, Vol. 7, March 2003.
9. Abdel-Ghafar, R., Morris, T., Ritchings, T., Wood, I., Detection and characterisation of the optic disk in glaucoma and diabetic retinopathy, Proceedings of Medical Image Understanding and Analysis, September 2004.
10. Pratt, W.K., Digital Image Processing, NY: Wiley, 1991.
Fig 6. Binary format of ophthalmologist’s hand-drawn tracing of blood vessels in Original Image B.
Fig 10: Binary format of ophthalmologist’s hand-drawn tracing of blood vessels in Original Image C.
Fig 1. Original Image A (from the STARE database)‏
Fig 5. Original Image B (from the STARE database)‏
Fig 9: Original Image B (from the STARE database)‏
Fig 3. Blood Vessel Segmentation Algorithm 1’s output image A. Degree of match to the hand-drawn image using…
Pratt’s figure of Merit: 0.6506
Signal to Noise ratio: 12.14
Root mean square error: 63.027
Fig 4. Blood Vessel Segmentation Algorithm 2’s output image A. Degree of match to hand-drawn image using…
Pratt’s figure of Merit: 0.6685
Signal to Noise ratio: 10.536
Root mean square error: 65.810
Fig 7. Blood Vessel Segmentation Algorithm 1’s output image B. Degree of match to the hand-drawn image using…
Pratt’s figure of Merit: 0.5361
Signal to Noise ratio: 11.11
Root mean square error: 70.967
Fig 8. Blood Vessel Segmentation Algorithm 2’s output image B. Degree of match to the hand-drawn image using…
Pratt’s figure of Merit: 0.5577
Signal to Noise ratio: 10.136
Root mean square error: 69.389
Fig 11. Blood Vessel Segmentation Algorithm 1’s output image C. Degree of match to the hand-drawn image using…
Pratt’s figure of Merit: 0.6418
Signal to Noise ratio: 11.669
Root mean square error: 66.545
Fig 12. Blood Vessel Segmentation Algorithm 2’s output image C. Degree of match to the hand-drawn image using…
Pratt’s figure of Merit: 0.5822
Signal to Noise ratio: 10.859
Root mean square error: 63.044
Fig 2. Binary format of ophthalmologist’s hand-drawn tracing of blood vessels in Original Image A.
Notes: <number>